## Slide 1: Cropland Inventory
Within the
St. Albans Bay Watershed

## Slide 2: Study Area

## Slide 3: Why?

## Slide 4: What Data was Collected?
  Acreage of Fields
  Tiled Fields
  Miles of Streams and Ditches
  Livestock Numbers
  Crop Rotations
  Crop Yields
  Soil Tests
  P-Index Ratings and Scores
  Manure Recommendations and Records
  Relating High and Very High Phosphorus Levels to Spreading Records

## Slide 5: Representation of Agricultural Lands

## Slide 6: Percentage of Agricultural Land Related to Farm Size

## Slide 7: Identifiable Tiled Agricultural Fields

## Slide 8: Waterway Conveyances
Add Map

## Slide 9: Comparing 1990 to 2014
Meals, D.M. 1992. Relating Land Use and Water Quality in the St. Albans Bay Watershed, Vermont. Pages 131 to 143 in 10-years of Controlling Agricultural Nonpoint Source Pollution Source: The RCWP Experience, National RCWP Symposium in Orlando, Florida.

## Slide 10: Contents of Nutrient Management Plans (NMPs)
Current Soil Test Results
Current Manure Analyses
Manure Production Information (# of animals, amount of manure, and amount of storage)
6 Different Types of Maps:
  Proximity, Conservation Plan, Nitrate Leaching, Topographic, Environmental Concerns, and Soil type.
RUSLE II Calculations
Crop rotations, cover cropping, and yield goals
Environmental factors that affect nutrient transport (P-Index)
Manure & fertilizer application to each field (timing, amount, method)
Recordkeeping
                =
Field by Field plan for meeting the nutrient needs of the crop while minimizing movement of the nutrients from the field.

## Slide 11: Fields Inventoried

## Slide 12: Crop Rotations
All Fields Inventoried
50% in Continuous Corn
40% in Corn/Hay Rotation
12% include Cover Crops in Rotation
Jewett Fields Inventoried
47% in Continuous Corn
41% in Corn/Hay Rotation
14% include Cover Crops in Rotation

## Slide 13: Rotations Being Followed?
Why is it important to follow recommended field rotations?
Not Being Followed:
20% Recommended: Corn Silage
  Actual: Alfalfa/grass, grass, or reseeding
17% Recommended: Alfalfa/grass, grass, or reseeding
  Actual: Corn Silage
13% Recommended: Corn Silage/Hay Rotation
  Actual: Continuous Corn Rotation
Not Being Followed:
25% Recommended: Corn Silage
  Actual: Alfalfa/grass, grass, or reseeding
19% Recommended: Alfalfa/grass, grass, or reseeding
  Actual: Corn Silage
15% Recommended: Corn Silage/Hay Rotation
  Actual: Continuous Corn Rotation

## Slide 14: Crop Yields
What could be beneficial about having actual yields above predicted yields?
What could be negative about having actual yields below predicted yields?

## Slide 15: Soil Test Completion

## Slide 16: Phosphorus Levels in Soil Tests
Optimum range: 4.1 – 7 ppm
n = 288
n = 126

## Slide 17: Soil Test Statistics (n = 288)
pH Levels
Potassium Levels
Aluminum Levels
% Organic Matter
Optimum range: 101-130 ppm
Optimum range for corn or hay : 6.0 – 7.0

## Slide 18: P Index Levels
P Index (aka Phosphorus Index) is a risk assessment tool to quantify the potential for phosphorus runoff from a field. The P Index helps to target critical source areas of potential P loss for greater management attention.

## Slide 19: High and Very High Phosphorus Levels Verse P-Index
All Fields
Jewett Fields

## Slide 20: Manure Samples (n = 13)
Total N
Ammonia (NH4 – N)
Phosphate (P2O5)
Potassium (K2O)
Total Solids (%)
UVM “Book Value”: 25 lbs./1000 gal
12 lbs./1000 gal
8 lbs./1000 gal
20 lbs./1000 gal
7 %

## Slide 21: Manure Records Kept in 2014?

## Slide 22: Manure Spreading on Fields
Recommended
Actual

## Slide 23: Manure Spreading Season

## Slide 24: Do Actual Manure Application Rates Match Recommended Manure Application Rates?

## Slide 25: Hay verse Corn Silage Applications

## Slide 26: Type of Rotation Having High or Excessive Phosphorus Levels

## Slide 27: High or Excessive Phosphorus Levels Related to Manure Spreading

## Slide 28: High or Excessive Phosphorus Levels Related to Manure Spreading Seasons

## Slide 29: Payments Connected to NMPs
VAAFM’s NMP
Cost-Share Program
NRCS’s Cost-Share
CAP Programs
Rate = $19.01/acre
Rate = $4.95/acre
Rate = $5.05/acre

## Slide 30: What can YOU do to help reduce phosphorus on YOUR farm fields?
Farmers in Jewett Work Together to Reduce Phosphorus Levels