## Slide 1: Assessment of Tile Drainage System Impacts to Lake Champlain and Phosphorus Loads in Tile Drainage in the Jewett Brook Watershed of St. Albans Bay
Date: January 8, 2018
Presented by: Dave Braun
Venue: Lake Champlain Research Conference
Funded by the Lake Champlain Basin Program

## Slide 2: This is a study in three parts:
Task 1: Tile Drainage Literature Review (Completed)
  Written by Don Meals and Julie Moore
  252 publications reviewed
  Used as a basis for VTANR’s tile drain report to legislature, January 2017
Task 2: Monitoring of Tile Drainage Systems (In Progress)
  Participation by 6 farmers
  Monitoring 12 tile drains (April 2017 – April 2018)
  Characterization of tile drainage systems
  Continuous flow measurement and composite water sample collection
  Analysis for total and dissolved P and total N
Task 3: P Load Estimation of Tile Drainage Systems (2018)
  Analysis of associations between water quality and agronomic variables
  Evaluation of Jewett Brook P load
  Assessment of tile drain P load significance

## Slide 3: Study Field and Tile Drainage System Characterization
Characterization Report (March 1, 2017) describes:
  Construction of tile drainage systems
  Surface inlets
  Crop production
  Soil types and soil test P
  Manure and fertilizer applications
 | Site | Area (A) | Crop | Soil Survey Data % of field, type, slope class, hydrologic group | Soil Test P | Fertilizer Application | Manure Application | Cover Crop
Farmer1 | JBT01 | 25 | 2016: Silage corn 2017: Soybean | 82%: Kingsbury clay, 0 to 3%, D 10%: Massena stony loam, 0 to 3%, C/D 8%: Kingsbury clay, 3 to 8%, D | 7.2 | 2016: starter at plant 2017: starter at plant | 2016: None 2017: None | 2016: None 2017: Unknown
Farmer1 | JBT02 | 4.7 | 2016: Silage corn 2017: Soybean | 69%: Kingsbury clay, 3 to 8%, D 31%: Kingsbury clay, 0 to 3%, D | 9.3 | 2016: starter at plant 2017: starter at plant | 2016: None 2017: None | 2016: None 2017: Unknown
Farmer1 | JBT04 | 5.7 | 2016: Silage corn 2017: Soybean | 100%: Kingsbury clay, 0 to 3%, D | 4.5 | 2016: starter at plant 2017: starter at plant | 2016: None 2017: None | 2016: None 2017: Unknown

## Slide 4: Inlet to JBT14 Tile Drain (3 tile drains have surface inlets; blind inlets also possible)

## Slide 5: JBT11 Monitoring Station

## Slide 6: Typical Instrument Shelter (JBT11)

## Slide 7: Waterflux 3000 Flowmeter at JBT11, April 20, 2017
TP: 14.7 µg/L
TDP: 9.7 µg/L
TN: 2.45 mg/L

## Slide 8: JBT01 flowing muddy, November 3, 2017
TP: 329 µg/L
TDP: 60.1 µg/L

## Slide 9: JBT06 field on October 27, 2017 after manure injection
TP: 1,884 µg/L
TDP: 1,576 µg/L

## Slide 10: Distributions of Total P EMCs (April – Nov., 2017)
JBT13: TP=35,295 µg/L (excluded)
Samples following manure application

## Slide 11: Questions:
Current study:
Associations between water quality and agronomic variables
Proportion of Jewett Brook P load contributed by tile drains
Three related research questions / farmer concerns
Are conditions in the Jewett Brook watershed representative of conditions in the wider Lake Champlain Basin?
Are surface inlets the main route for P transport to tile drains, particularly where we find high P concentrations following manure application?
Given multiple trade offs between surface runoff and subsurface drainage, is the net effect of tile drainage increased or decreased P export?

## Slide 12: Thank you.
Dave Braun
dbraun@stone-env.com
(802)272-8819

## Slide 13: Phosphorus Removal from Tile Drainage Water Using Media Filters
Date: January 8, 2018
Presented by: Dave Braun
Venue: Lake Champlain Research Conference
Funded by a Conservation Innovation Grant from USDA NRCS to FNLC

## Slide 14: System Installation
Filter B:
Crushed limestone “bedding sand”
Filter A: Drinking water treatment residuals

## Slide 15: TP Percent Removal Increases with Higher Influent P

## Slide 16: Results
INFLOW: P concentrations were generally high
  Median TP EMC = 345 µg/L (24 composite samples)
  On average, 86% was dissolved
OUTFLOW: Both filters reduced P
  DWTR: 69% (median TP EMC = 118 µg/L)
  Limestone: 54% (median TP EMC = 220 µg/L)
  Neither media appeared to approach P saturation
  Neither media consistently removed N
  Both media became clogged with sediment
  Over 11 months, their maximum filtration rates declined by 92% (from 13 GPM to 1.0 GPM)
  Installed cost = $5K per filter

## Slide 17: Conclusions
Both filters removed P, however DWTR outperformed crushed limestone
Both filters clogged with sediment too quickly
  Design challenges
          Huge water volumes
          Relatively low P concentrations (usually)
          Minimal elevation difference between tile and ditch
          Sediment
          No electricity
Recommendations:
Select media with greater hydraulic conductivity (>0.3 cm/s; gravel range)
Install media in lined trenches to enable upscaling and reduce cost
Install sedimentation chamber upstream of filter
Incorporate means to backflush the filter of accumulated sediments

## Slide 18: Thank you
Dave Braun
dbraun@stone-env.com
(802)272-8819