## Slide 1: Assessment of Phosphorus Loads from Tile Drainage in the Jewett Brook Watershed of St. Albans Bay and Addison County This project is funded by the Lake Champlain Basin Program
Venue: Project Advisory Committee Meeting #1
Date: April 24, 2019
Presented by: Dave Braun

## Slide 2: Study objectives
Evaluate associations between agronomic variables and tile drain P concentrations and P loading
Assess the proportion of the Jewett Brook P load contributed by tile drains
Monitoring program:
  Participation by 6 farmers
  Monitoring 12 tile drains (April 2017 – April 2018)
  Characterized of tile drainage systems
  Measured flow continuously and collected composite water samples
  Grab sampling over winter months
  Analysis for total and dissolved P and total N
This study was not designed to answer a third question of great interest in the Lake Champlain Basin: Does tile drainage increase or decrease total loading (surface plus subsurface) of phosphorus?

## Slide 3: Tile drainage systems monitored
  All 12 systems monitored are standard, perforated, corrugated drain pipe.
  All study fields have patterned drainage except JBT16, which has a dendritic (branching) system.
  Drain spacing is in the typical range of 25–40 feet, with the exception of JBT18 and JBT19, which have 80-foot spacing.
  The tile drains range from 3–5 feet below ground
  The outfalls range in diameter from 4–12 inches.
  Most were installed within the last decade.

## Slide 4: JBT11 monitoring station

## Slide 5: Waterflux 3000 flowmeter at JBT11, April 20, 2017

## Slide 6: P concentrations in tile discharge
 | [TP] (mg/L) | [TDP] (mg/L)
Range | 18 – 6,977 | 9 – 4,826
Median | 150 | 59
Mean | 140 | 63
N (months) | 156 | 156
TP concentrations in JBW tile drainage comparable to range observed in NY, OH, WI, Quebec, and Ontario
 | Areal TP load (kg/ha/yr) | Areal TDP load (kg/ha/yr)
Range | 0.12 – 1.12 | 0.083 – 0.56
Median | 0.54 | 0.20
Mean | 0.56 | 0.27
95% C.I. | 0.37 – 0.74 | 0.17 – 0.38
P loads in tile discharge
P loads in JBW tile drainage comparable to loads observed elsewhere: | 
Quebec (LCB): | 0.61 kg TP/ha/yr
Ohio: | 0.28 – 0.92 kg TP/ha/yr

## Slide 7: Effects of land use/ag management
Manure application
Y-axis scale excludes high outlier at JBT13 on May 16, 2017 (TP=35,295 µg/L)
Median [TP] in Jewett Brook
Sample following manure application

## Slide 8: JBT06 field on October 27, 2017 after manure injection
TP: 1,884 µg/L
TDP: 1,576 µg/L

## Slide 9: P loads from JBW tile drainage
 | Row Crop |  | Hay | 
 | Areal TP load (kg/ha/yr) | Areal TDP load (kg/ha/yr) | Areal TP load (kg/ha/yr) | Areal TDP load (kg/ha/yr)
Median | 0.65 | 0.29 | 0.25 | 0.10
95% C.I. | 0.44 – 0.86 | 0.19 – 0.45 | 0.14 – 0.69 | 0.042 – 0.31
 | TP (kg/yr) | TDP (kg/yr)
 | Median | Median
Row crop | 580 | 258
Hay | 84 | 34
TOTAL | 664 | 292
We then calculated total mass loads of phosphorus from tile drains on the Jewett Brook watershed, using the areal P loads above and the acreage of tile drained row cropland and hayland in the watershed.

## Slide 10: Conclusions
P concentrations and loads per hectare in tiles draining row crops tended to be higher than levels observed from hayland.
Total P and total dissolved P tended to be higher from fields that had received some manure in 2017, compared to fields that were not manured. Episodic very high P concentrations were observed when wet-weather tile flow coincided with manure application.
Tile drainage was estimated to contribute 664 kg TP of the 3,404 kg TP exported from Jewett Brook during the monitored year, and 292 kg TDP of the 2,488 kg TDP.
While the aerial total phosphorus loading rates of 0.65 kg/ha/yr from row cropland and 0.25 kg/ha/yr from hayland were comparable to literature values, the cumulative contribution of 20% (up to 35%) of the annual TP load was somewhat lower than expected. Nevertheless, these contributions are not insignificant.
These results suggest that it will be difficult to accomplish target reductions of agricultural P loads to Lake Champlain without considering tile drain contributions.
              Thank You

## Slide 11: Typical instrument shelter (JBT11)