## Slide 1: Assessment of Phosphorus Loads from Tile Drainage in the Jewett Brook Watershed of St. Albans Bay This project was funded by the Lake Champlain Basin Program
Venue: The Science of Water Quality—Meeting of the Minds
Date: May 1, 2019
Presented by: Dave Braun

## Slide 2: Jewett Brook Watershed
  2389 ha (9.2 square miles)
  61% of the watershed area is tiled drained (22% pattern and 39% random) (VAAFM 2015 Saint Albans Bay Watershed Cropland Inventory)
  Could tile drainage contribute to the high P concentrations and loads?

## Slide 3: Tile drainage primer
Tile drainage offers many benefits, both agronomic and environmental:
In fields otherwise too wet to farm efficiently, tile drainage enables:
Timely equipment access
Timely application of conservation measures
More efficient nutrient uptake by crops
Increased crop yields
Reduced soil erosion and compaction
Tile drainage dramatically changes the hydrologic behavior of a field, enhancing infiltration and ground water transmission and reducing surface runoff.

## Slide 4: Study objectives
Evaluate associations between agronomic variables and tile drain P concentrations and P loading
Assess the proportion of the Jewett Brook P load contributed by tile drains
Monitoring program:
  6 farmers participated
  12 tile drains monitored April 2017 – April 2018
  Characterized tile drainage systems
  Measured flow continuously and collected composite water samples
  Grab sampling over winter months
  Analysis for total and dissolved P and total N
This study was not designed to answer a third question of great interest in the Lake Champlain Basin:
      Does tile drainage increase or decrease total loading of phosphorus (surface plus subsurface)?

## Slide 5: Tile drainage systems monitored
  All 12 systems monitored are standard, perforated, corrugated drain pipe.
  All study fields have patterned drainage except JBT16, which has a “random” (branching) system.
  Spacing of tile lines is in the typical range of 25–40 feet, with the exception of JBT18 and JBT19, which have 80-foot spacing.
  Tile drains range from 3–5 feet below ground.
  Outfalls range in diameter from 4–12 inches.
  Most were installed within the last decade.

## Slide 6
JBT14 “diversion”
monitoring station
Inlets
    JBT06 is the only field with functioning surface inlets
    Diversions present in JBT14 and JBT16
    Blind inlets possible but not found
FLOW

## Slide 7: JBT11 monitoring station

## Slide 8: Typical instrument shelter (JBT11)

## Slide 9: Waterflux 3000 flowmeter at JBT11
FLOW
FLOW

## Slide 10: Tile discharge
TP: 14.7 µg/L
TDP: 9.7 µg/L
TN: 2.45 mg/L
Chart: Flow rate (L/min)

## Slide 11: Annual mean P concentrations in tile discharge1
 | [TP] (µg/L) | [TDP] (µg/L)
Range | 45 – 1,166 | 23 – 762
Median | 185 | 90
Mean | 260 | 141
TP concentrations in JBW tile drainage comparable to range observed in NY, OH, WI, Quebec, and Ontario
 | Areal TP load (kg/ha/yr) | Areal TDP load (kg/ha/yr)
Range | 0.12 – 1.12 | 0.083 – 0.56
Median | 0.54 | 0.20
Mean | 0.56 | 0.27
95% C.I. | 0.37 – 0.74 | 0.17 – 0.38
Annual areal P loads in tile discharge
TP loads in JBW tile drainage comparable to loads observed elsewhere: | 
Quebec (LCB): | 0.61 kg/ha/yr
Ohio: | 0.28 – 0.92 kg/ha/yr
1. Calculated by site as total annual P load / total discharge volume

## Slide 12: Dissolved P fraction in tile discharge
Overall, ~50% of TP occurred as TDP
Varied among monitored fields from <30% to >80%
Seasonal variation not strong

## Slide 13: Effects of land use/ag management
Looked at associations between P concentration and loading and agronomic variables:
      2017 crop: row crop versus hay
      2017 manure application: Yes or No
      Cover crop on corn: Yes or No
      Soils: clay or loam
      Field size

## Slide 14: Effects of land use/ag management: CROP TYPE
Areal loads of TP and TDP were significantly higher from row cropland compared to hayland. TDP concentrations was also significantly higher from row cropland compared to hayland.
Areal TP load (kg/ha/yr)
row crop
hay
Areal TP load (kg/ha/yr)

## Slide 15: Effects of land use/ag management: MANURE
Nonsignificant tendency for higher P concentrations from manured fields
Nonsignificant tendency for greater tile discharge and higher P loading from manured fields, but pattern confounded by field size/crop
manure
no manure
Areal TP load (kg/ha/yr)

## Slide 16: Effects of land use/ag management: MANURE
Y-axis scale excludes high outlier at JBT13 on May 16, 2017 (TP=35,295 µg/L)
Median [TP] in Jewett Brook
Sample following manure application

## Slide 17: JBT06 field on October 27, 2017 after manure injection
TP: 1,884 µg/L
TDP: 1,576 µg/L

## Slide 18: Effects of land use/ag management: SOILS, FIELD SIZE, COVER CROP (presence/absence)
Few significant or interesting associations (low n, confounding variables)
Non-significant associations with soils may have been due to low variability among study fields. Most study fields have both clay (Covington and/or Kingsbury) and loam components and none have sand. 7 fields are principally clays 5 fields are principally loams

## Slide 19: JBW P load estimates
  Used the USGS program LOADEST to calculate P loading rates in Jewett Brook over the monitoring period
  TP load from the monitored portion of the JBW was 1,913 kg/yr (1,628 – 2,234 kg/yr).
  TDP load from the monitored portion of the JBW was 1,398 kg/yr (1,278 – 1,734 kg/yr).
USGS stream gauge

## Slide 20: P loads from JBW tile drainage
 | Row Crop (1,398 ha) |  | Hay (603 ha) | 
 | Areal TP load (kg/ha/yr) | Areal TDP load (kg/ha/yr) | Areal TP load (kg/ha/yr) | Areal TDP load (kg/ha/yr)
Median | 0.65 | 0.29 | 0.25 | 0.10
95% C.I. | 0.44 – 0.86 | 0.19 – 0.45 | 0.14 – 0.69 | 0.042 – 0.31
 | TP (kg/yr) |  | TDP (kg/yr) | 
 | Median | 95% CI | Median | 95% CI
Row crop | 909 | 617 – 1198 | 404 | 267 – 622
Hay | 150 | 83 – 413 | 61 | 25 – 184
TOTAL | 1,059 | 700 – 1612 | 465 | 292 – 807
We then calculated total mass loads of phosphorus from tile drains in the Jewett Brook watershed, using the areal P loads above and the acreage of tile drained row cropland and hayland in the watershed.

## Slide 21: Significance of tile drain P loading
 | Mean annual load (kg/yr) | 95% C.I. (kg/yr)
TP | 3,101 | 2,639 – 3,621
TDP | 2,266 | 2,071 – 2,811
Jewett Brook P loads extrapolated to entire JBW (2389 ha)
 | Mean annual load (kg/yr) | 95% CI (kg/yr)
TP | 806 | 667 – 1593
TDP | 355 | 276 – 792
Estimated P loads in tile discharge for entire JBW
 | Tile load % of total | Range
TP | 26% | 15 – 45%
TDP | 16% | 8.0 – 29%
Proportion of total JBW P loads contributed by tile drains

## Slide 22: Conclusions
P concentrations and loads per hectare in tiles draining row crops tended to be higher than levels observed from hayland.
Total P and total dissolved P tended to be higher from fields that had received some manure in 2017, compared to fields that were not manured. Episodic very high P concentrations were observed when wet-weather tile flow coincided with manure application.
Tile drainage was estimated to contribute 1,059 kg TP of the 3,101 kg TP exported from Jewett Brook during the monitored year, and 465 kg TDP of the 2,266 kg TDP.
The aerial total phosphorus loading rates of 0.65 kg/ha/yr from row cropland and 0.25 kg/ha/yr from hayland were comparable to literature values, as was the cumulative contribution of 34% of the annual TP load.
These results suggest that it will be difficult to accomplish target reductions of agricultural P loads to Lake Champlain without considering tile drain contributions.
THESE FOREGOING VALUES ARE SUBJECT TO CHANGE PENDING FINAL RESOLUTION OF TILE DRAINED CROPLAND AREA.
              Thank You

## Slide 23: Monitoring manhole installation (ACT4)

## Slide 24: Thel-mar weir and level sensor in ACT3 manhole

## Slide 25: Benchtop testing of filter media