## Slide 1: Assessment of Phosphorus Loads from Tile Drainage in the Jewett Brook Watershed of St. Albans Bay This project was funded by the Lake Champlain Basin Program
Venue: Vermont Agricultural Water Quality Partnership
Date: February 22, 2019
Presented by: Dave Braun

## Slide 2: Jewett Brook Watershed
  2096 ha (8.1 square miles)
  About 52% of the land is tiled drained (VAAFM 2015 Saint Albans Bay Watershed Cropland Inventory)
  Could tile drainage contribute to the high P concentrations and loads?

## Slide 3: Tile drainage primer
Tile drainage offers many benefits, both agronomic and environmental:
In fields otherwise too wet to farm efficiently, tile drainage enables:
Reduced soil compaction
Reduced soil erosion
Timely equipment access
Timely application of conservation measures
More efficient nutrient uptake by crops
Increased crop yields
Tile drainage dramatically changes the hydrologic behavior of a field, enhancing infiltration and ground water transmission and reducing surface runoff.

## Slide 4: Study objectives
Evaluate associations between agronomic variables and tile drain P concentrations and P loading
Assess the proportion of the Jewett Brook P load contributed by tile drains
Monitoring program:
  Participation by 6 farmers
  Monitoring 12 tile drains (April 2017 – April 2018)
  Characterized of tile drainage systems
  Measured flow continuously and collected composite water samples
  Grab sampling over winter months
  Analysis for total and dissolved P and total N
This study was not designed to answer a third question of great interest in the Lake Champlain Basin: Does tile drainage increase or decrease total loading (surface plus subsurface) of phosphorus?

## Slide 5: Tile drainage systems monitored
  All 12 systems monitored are standard, perforated, corrugated drain pipe.
  All study fields have patterned drainage except JBT16, which has a dendritic (branching) system.
  Drain spacing is in the typical range of 25–40 feet, with the exception of JBT18 and JBT19, which have 80-foot spacing.
  The tile drains range from 3–5 feet below ground
  The outfalls range in diameter from 4–12 inches.
  Most were installed within the last decade.

## Slide 6: JBT11 monitoring station

## Slide 7: Waterflux 3000 flowmeter at JBT11, April 20, 2017

## Slide 8: Tile discharge
TP: 14.7 µg/L
TDP: 9.7 µg/L
TN: 2.45 mg/L
Chart: Flow rate (L/min)

## Slide 9: P concentrations in tile discharge
 | [TP] (mg/L) | [TDP] (mg/L)
Range | 18 – 6,977 | 9 – 4,826
Median | 150 | 59
Mean | 140 | 63
N (months) | 156 | 156
TP concentrations in JBW tile drainage comparable to range observed in NY, OH, WI, Quebec, and Ontario
 | Areal TP load (kg/ha/yr) | Areal TDP load (kg/ha/yr)
Range | 0.12 – 1.12 | 0.083 – 0.56
Median | 0.54 | 0.20
Mean | 0.56 | 0.27
95% C.I. | 0.37 – 0.74 | 0.17 – 0.38
P loads in tile discharge
P loads in JBW tile drainage comparable to loads observed elsewhere: | 
Quebec (LCB): | 0.61 kg TP/ha/yr
Ohio: | 0.28 – 0.92 kg TP/ha/yr

## Slide 10: Effects of land use/ag management
Looked at associations between P concentration and loading and agronomic variables:
      2017 crop: row crop versus hay
      2017 manure application: Yes or No
      Cover crop on corn: Yes or No
      Soils: clay or loam
      Field size

## Slide 11: Effects of land use/ag management
Crop
Areal loads of TP and TDP were significantly higher from row cropland compared to hayland. TDP concentrations was also significantly higher from row cropland compared to hayland.
row crop
hay
Areal TP load (kg/ha/yr)

## Slide 12: Effects of land use/ag management
Manure application
Nonsignificant tendency for higher P concentrations from manured fields
Nonsignificant tendency for greater tile discharge and higher P loading from manured fields, but pattern confounded by field size/crop
manure
no manure
Areal TP load (kg/ha/yr)

## Slide 13: Effects of land use/ag management
Manure application
Y-axis scale excludes high outlier at JBT13 on May 16, 2017 (TP=35,295 µg/L)
Median [TP] in Jewett Brook
Sample following manure application

## Slide 14: JBT06 field on October 27, 2017 after manure injection
TP: 1,884 µg/L
TDP: 1,576 µg/L

## Slide 15: Effects of land use/ag management
Cover crop, soils, and field size
Few significant or interesting associations (low n, confounding variables)

## Slide 16: P loads from JBW tile drainage
 | Row Crop |  | Hay | 
 | Areal TP load (kg/ha/yr) | Areal TDP load (kg/ha/yr) | Areal TP load (kg/ha/yr) | Areal TDP load (kg/ha/yr)
Median | 0.65 | 0.29 | 0.25 | 0.10
95% C.I. | 0.44 – 0.86 | 0.19 – 0.45 | 0.14 – 0.69 | 0.042 – 0.31
 | TP (kg/yr) | TDP (kg/yr)
 | Median | Median
Row crop | 580 | 258
Hay | 84 | 34
TOTAL | 664 | 292
We then calculated total mass loads of phosphorus from tile drains on the Jewett Brook watershed, using the areal P loads above and the acreage of tile drained row cropland and hayland in the watershed.

## Slide 17: JBW P loads
JBW load estimates
    Used the USGS program LOADEST to calculate P loading rates in Jewett Brook over the monitoring period
    TP load from the monitored portion of the JBW was 1,913 kg/yr (1,628 – 2,234 kg/yr).
    TDP load from the monitored portion of the JBW was 1,398 kg/yr (1,278 – 1,734 kg/yr).
USGS stream gauge

## Slide 18: Significance of tile P loads
 | Mean annual load (kg/yr) | 95% C.I. (kg/yr)
TP | 3,404 | 2,898 – 3,976
TDP | 2,488 | 2,275 – 3,086
Jewett Brook P loads extrapolated to entire JBW
 | Mean annual load (kg/yr) | 95% CI (kg/yr)
TP | 664 | TBD
TDP | 292 | TBD
Estimated P loads in tile discharge for entire JBW
 | Tile load % of total | Range
TP | 20% | 11 – 35%
TDP | 12% | 6.0 – 20%
Proportion of total JBW P loads contributed by tile drains

## Slide 19: Conclusions
P concentrations and loads per hectare in tiles draining row crops tended to be higher than levels observed from hayland.
Total P and total dissolved P tended to be higher from fields that had received some manure in 2017, compared to fields that were not manured. Episodic very high P concentrations were observed when wet-weather tile flow coincided with manure application.
Tile drainage was estimated to contribute 664 kg TP of the 3,404 kg TP exported from Jewett Brook during the monitored year, and 292 kg TDP of the 2,488 kg TDP.
While the aerial total phosphorus loading rates of 0.65 kg/ha/yr from row cropland and 0.25 kg/ha/yr from hayland were comparable to literature values, the cumulative contribution of 20% (up to 35%) of the annual TP load was somewhat lower than expected. Nevertheless, these contributions are not insignificant.
These results suggest that it will be difficult to accomplish target reductions of agricultural P loads to Lake Champlain without considering tile drain contributions.
              Thank You

## Slide 20: Typical instrument shelter (JBT11)

## Slide 21: P loads from JBW tile drainage
Method 1
 | Areal TP load (kg/ha/yr) | Areal TDP load (kg/ha/yr)
Median | 0.541 | 0.199
95% C.I. | 0.368 – 0.743 | 0.166 – 0.378
 | Median Export (kg/yr) | 95% C.I. (kg/yr)
TP | 458 | 311 - 638
TDP | 168 | 140 - 320

## Slide 22: Significance of tile P loads from JBW
Approach 1 (USGS station)
 | Mean annual tile load (kg/yr) | 95% CI (kg/yr)
TP | 280 | 190 – 384
TDP | 103 | 86 - 195
 | Tile load % of total | Range
TP | 15% | 8.5 – 24%
TDP | 7% | 5 – 15%
Proportion of total JBW P loads above USGS station contributed by tile drains
Estimated P loads in tile discharge above USGS station (tiled area = 517 ha)