## Slide 1: Assessment of Phosphorus Loads from Tile Drainage in the Jewett Brook Watershed of St. Albans Bay
Venue: LCBP Technical Advisory Committee
Date: February 6, 2019
Presented by: Dave Braun and Don Meals

## Slide 2: Tile drainage
Subsurface drainage is an essential management practice on many farm fields.
In fields otherwise too wet to farm efficiently, tile drainage enables:
Reduced soil compaction
Reduced soil erosion
More efficient nutrient uptake by crops
Timely equipment access
Timely application of conservation measures
Increased crop yields
Tile drainage dramatically changes the hydrologic behavior of a field, reducing surface runoff by enhancing infiltration and ground water transmission.

## Slide 3: This was a study in three parts:
Task 1: Tile Drainage Literature Review (Completed)
  Written by Don Meals and Julie Moore
  252 publications reviewed
  Used as a basis for VTANR’s required tile drain report to legislature, January 2017
Task 2: Monitoring of Tile Drainage Systems (Completed)
  Participation by 6 farmers
  Monitoring 12 tile drains (April 2017 – March 2018)
  Characterization of tile drainage systems
  Continuous flow measurement and composite water sample collection
  Analysis for total and dissolved P and total N
Task 3: P Load Estimation of Tile Drainage Systems (Completed)
  Analysis of associations between water quality and agronomic data
  Evaluation of Jewett Brook P load
  Assessment of tile drain P load significance

## Slide 4: Identifiable Tiled Agricultural Fields from Vermont AAFM’s 2015 Cropland Inventory
We calculate 40.3%

## Slide 5: Study field and tile drainage system characterization
Site Characterization Report (March 1, 2017) describes:
  Construction of tile drainage systems
  Surface inlets to tile drains
  Crop production in study fields
  Field soil types
  Soil Test P in study fields
  Manure and fertilizer applications
 | Site | Area (A) | Crop | Soil Survey Data % of field, type, slope class, hydrologic group | Soil Test P | Fertilizer Application | Manure Application | Cover Crop
Farmer1 | JBT01 | 25 | 2016: Silage corn 2017: Soybean | 82%: Kingsbury clay, 0 to 3%, D 10%: Massena stony loam, 0 to 3%, C/D 8%: Kingsbury clay, 3 to 8%, D | 7.2 | 2016: starter at plant 2017: starter at plant | 2016: None 2017: None | 2016: None 2017: Unknown
Farmer1 | JBT02 | 4.7 | 2016: Silage corn 2017: Soybean | 69%: Kingsbury clay, 3 to 8%, D 31%: Kingsbury clay, 0 to 3%, D | 9.3 | 2016: starter at plant 2017: starter at plant | 2016: None 2017: None | 2016: None 2017: Unknown
Farmer1 | JBT04 | 5.7 | 2016: Silage corn 2017: Soybean | 100%: Kingsbury clay, 0 to 3%, D | 4.5 | 2016: starter at plant 2017: starter at plant | 2016: None 2017: None | 2016: None 2017: Unknown

## Slide 6: Tile drainage system construction
  All 12 systems selected are standard, perforated, corrugated drain pipe.
  Most were installed within the last decade.
  The outfalls range in diameter from 4–12 inches.
  9 of the 12 tile drains discharge to ditches. The 3 remaining (JBT01, JBT02, and JBT04) discharge directly to Jewett Brook.
  The tile drains range from 3–5 feet below ground, with most in the 3–4 feet range.
  All study fields have patterned drainage except JBT16, which has a dendritic (branching) system.
  Drain spacing is in the typical range of 25–40 feet, with the exception of JBT18 and JBT19, which have 80-foot spacing.

## Slide 7: Surface inlet to JBT14 tile drain (3 systems have known inlets; blind inlets also possible)

## Slide 8: Monitoring manhole construction

## Slide 9: Waterflux 3000 flowmeter at JBT11, April 20, 2017

## Slide 10: JBT11 monitoring station

## Slide 11: Typical instrument shelter (JBT11)

## Slide 12: Tile discharge
TP: 14.7 µg/L
TDP: 9.7 µg/L
TN: 2.45 mg/L
Chart: Flow rate (L/min)

## Slide 13: Tile discharge
Tile drainflow was lowest August-September 2017 and tended to be high May – July 2017 and January – April 2018.

## Slide 14: Tile discharge
Tile drainflow varied across monitored fields

## Slide 15: [P] in tile discharge
 | [TP] (mg/L) | [TDP] (mg/L)
Range | 18 – 6,977 | 9 – 4,826
Median | 150 | 59
Mean | 140 | 63
N (months) | 156 | 156
JBW tile outlets
Location | Land Use | [TP] mg/L | [SRP] mg/L
NY | Corn | 110 – 9,800 | 
NY | Corn |  | 9 – 441
Que | Corn-soybeans | 10 – 130 | 10 – 30
Que |  | 60 – 370 | 
Que | Corn | 200 | 40
Que | Corn | 11 – 53 | 1 – 12
Que | Corn, grains, grass | <1 – 2,726 | 
Elsewhere in LCB
[TP] in JBW tile drainage also comparable to range observed in OH, WI, and Ontario

## Slide 16: [P] in tile discharge
[P] varied across monitored fields

## Slide 17: [P] in tile discharge
[P] varied across months, but less than across fields

## Slide 18: [P] in tile discharge
Correlation between tile discharge and [P] weak, inconsistent, and not always positive

## Slide 19: [P] in tile discharge
Overall, ~50% of TP occurred as TDP
Varied among monitored fields from <30% to >80%
Seasonal variation not strong

## Slide 20: P loads in tile discharge
 | Areal TPx (kg/ha/yr) | Areal TDPx (kg/ha/yr)
Range | 0.122 – 1.124 | 0.083 – 0.556
Median | 0.541 | 0.199
Mean | 0.555 | 0.272
95% C.I. | 0.368 – 0.743 | 0.166 – 0.378
P loads in JBW tile discharge comparable to loads observed elsewhere:
Quebec (LCB) 0.61 kg TP/ha/yr
Ohio 0.28 – 0.92 kg TP/ha/yr

## Slide 21: P loads in tile discharge
P load in tile discharge varied across monitored fields

## Slide 22: P loads in tile discharge
P load in tile discharge varied across months, primarily driven by discharge variation

## Slide 23: Effects of land use/ag management
Looked at associations between [P], P export and land use/management variables:
      Presence of surface inlet(s): Y or N
      2017 crop: soybeans, corn silage, hay, alfalfa
      2017 manure application: Y or N
      Cover crop on corn: Y or N
      Soils: clay or loam
      Field size

## Slide 24: Effects of land use/ag management
Surface inlet(s)
[P] not significantly associated with presence of surface inlets

## Slide 25: Effects of land use/ag management
Surface inlet(s)
[P] not significantly associated with presence of surface inlets
Tile discharge higher from systems with surface inlet(s)

## Slide 26: Effects of land use/ag management
Surface inlet(s)
[P] not significantly associated with presence of surface inlets
Tile discharge higher from systems with surface inlet(s)
P export tended to be higher from systems with surface inlet(s)

## Slide 27: Effects of land use/ag management
Crop
No significant associations observed between specific 2017 crop and [P], tile discharge, or P load in tile flow (low n)
Annual tile discharge tended to be higher from corn fields than from other crops, but confounded by field size
Aggregating fields by row crop (corn + soybeans) vs. hay (hay + alfalfa) showed that areal loads of TP and TDP tended to be significantly higher from row cropland compared to hayland. TDP concentration was also significantly higher from row cropland compared to hayland.

## Slide 28: Effects of land use/ag management
Manure application
Nonsignificant tendency for higher [P] from manured fields
Nonsignificant tendency for greater tile discharge and higher P export from manured fields, but pattern confounded by field size/crop

## Slide 29: Effects of land use/ag management
Manure application
Y-axis scale excludes high outlier at JBT13 on May 16, 2017 (TP=35,295 µg/L)

## Slide 30: JBT06 field on October 27, 2017 after manure injection
TP: 1,884 µg/L
TDP: 1,576 µg/L

## Slide 31: Effects of land use/ag management
Cover crop
No significant effects suggested for presence of cover crop
Low n, confounded by field size

## Slide 32: Effects of land use/ag management
Cover crop
No significant effects suggested for presence of cover crop
Low n, confounded by field size
Soils
No significant (or even suggestive) differences in [P], tile discharge, or P export from fields with predominantly clay soils compared to fields with a majority of loam soils.

## Slide 33: Effects of land use/ag management
Cover crop
No significant effects suggested for presence of cover crop
Low n, confounded by field size
Soils
No significant (or even suggestive) differences in [P], tile discharge, or P export from fields with predominantly clay soils compared to fields with a majority of loam soils.
Field size
Mean [P] did not vary significantly with field size
Tile discharge strongly correlated with field size
P export strongly correlated with field size, but NOT areal export
Significant positive correlation between field size and % TDP

## Slide 34: P loads from JBW tile drainage
Estimation methods
    Median and 95% CI of areal P loads from all monitored JBW tiled fields
    VAAFM data on “presence of tile” for the entire JBW (2096 ha) with fields clipped to watershed boundaries  845.5 ha of tile-drained cropland
    Method 1: applied areal P export from all monitoring data combined to all tile-drained fields in JBW
    Method 2: applied different areal P export values to tile-drained row crop and hayland, summed for all JBW tile-drained cropland

## Slide 35: P loads from JBW tile drainage
Method 1
 | Areal TP load (kg/ha/yr) | Areal TDP load (kg/ha/yr)
Median | 0.541 | 0.199
95% C.I. | 0.368 – 0.743 | 0.166 – 0.378
 | Median Export (kg/yr) | 95% C.I. (kg/yr)
TP | 458 | 311 - 638
TDP | 168 | 140 - 320

## Slide 36: P loads from JBW tile drainage
Method 2
 | Row Crop (RC) |  | Hay (H) | 
 | Areal TP load (kg/ha/yr) | Areal TDP load (kg/ha/yr) | Areal TP load (kg/ha/yr) | Areal TDP load (kg/ha/yr)
Median | 0.650 | 0.289 | 0.249 | 0.101
95% C.I. | 0.441 – 0.857 | 0.191 – 0.445 | 0.138 – 0.686 | 0.042 – 0.306
 | TP (kg/yr) |  | TDP (kg/yr) | 
 | Median | 95% C.I. | Median | 95% C.I.
Row crop | 399 | 270.8 – 526.2 | 177 | 117.3 – 273.2
Hay | 58 | 32.0 – 158.8 | 23 | 9.7 – 70.8
TOTAL | 458 | 302.8 – 685.0 | 201 | 127.0 – 344.0

## Slide 37: JBW P loads
Estimation methods (analysis by Eric Smeltzer)
    Monthly and annual mean P loading rates from Jewett Brook, May 2017 - April 2018, estimated from:
      Stream discharge measurements obtained at USGS station on Lower Newton Rd. (969 ha of JBW) during the period January 2017 - September 2018.
      [P] measurements from VT DEC LC Long-Term Monitoring
    Used the USGS program LOADEST to calculate P loading rates in Jewett Brook from the stream flow and P concentration data

## Slide 38: JBW P loads
JBW load estimates
    TP load from the monitored portion of the JBW over the annual period was 1,913 kg/yr (1,628 – 2,234 kg/yr).
    TDP load from the monitored portion of the JBW over the annual period was 1,398 kg/yr (1,278 – 1,734 kg/yr).

## Slide 39: Significance of tile P loads from JBW
Estimation methods
    Approach 1
      Recompute estimates of annual P loads from tile discharge for the tile drained cropland within 969 ha drainage area captured at the USGS station on Lower Newton Road. Direct comparison between tile drainage P loads in Jewett Brook estimated from tile monitoring data with estimated P loads in Jewett Brook from the same drainage area, although not from the entire JBW.
    Approach 2
      Compare estimates of annual P loads from tile discharge for all the 845.5 ha of tiled cropland within the entire JBW against annual P loads in Jewett Brook extrapolated from the USGS monitored area (1180 ha) to the entire watershed (2096 ha) by a simple area ratio.

## Slide 40: Significance of tile P loads from JBW
Approach 1 (USGS station)
 | Mean annual tile load (kg/yr) | 95% CI (kg/yr)
TP | 280 | 190 – 384
TDP | 103 | 86 - 195
 | Tile load % of total | Range
TP | 15% | 8.5 – 24%
TDP | 7% | 5 – 15%
Proportion of total JBW P loads above USGS station contributed by tile drains
Estimated P loads in tile discharge above USGS station (tiled area = 517 ha)

## Slide 41: Significance of tile P loads from JBW
Approach 2 (extrapolated to Jewett Brook Watershed)
 | Mean annual load (kg/yr) | 95% C.I. (kg/yr)
TP | 3,404 | 2,898 – 3,976
TDP | 2,488 | 2,275 – 3,086
Jewett Brook P loads extrapolated to entire JBW (drainage area = 1180 ha)
 | Mean annual load (kg/yr) | 95% CI (kg/yr)
TP | 458 | 311 – 638
TDP | 168 | 140 - 320
Estimated P loads in tile discharge for entire JBW (tiled area = 846 ha)
 | Tile load % of total | Range
TP | 13% | 8 – 22%
TDP | 7% | 4.5 – 14%
Proportion of total JBW P loads contributed by tile drains

## Slide 42: Conclusions
Monitored tile drains flowed continuously in late winter and spring periods, whereas in summer and early fall, the tile drains flowed only in response to rain events, with little or no flow between rains.
Tile discharge exhibited variable and sometimes high [P], averaging 140 mg/LTP and 63 mg/L TDP, but up to 6,977 mg/L TP and 4,826 mg/L TDP at times. Average [P] in JBW tile drainage was in a comparable range to literature values; peak [P] in JBW tended to be higher than values reported elsewhere.
No clear seasonal patterns in [TP] or [TDP] in tile discharge were observed, nor were strong positive correlations between [P] and tile discharge.
On average across all monitored tile outlets, about 50% of TP was in the dissolved form; the proportion of TDP, however, varied among the monitored tile systems, ranging from a low of ~30% in systems draining fine-textured soils to a high of ~80% in systems draining cornfields in long-term no-till practice.
Tile discharge in this portion of the LCB can carry significant levels of P directly to surface waters. Dissolved P can be an important form of P in tile drainage under some circumstances, but particulate P can make up a surprisingly large fraction of TP in drainage water

## Slide 43: Conclusions
Presence of surface inlets in a tile system did not influence [P], but high tile discharge in those systems resulted in significantly higher P export from tile systems with surface inlets.
Monitoring data suggest that [P] and P export per hectare in tile systems draining row crops tend to be higher than levels observed from hayland.
There was a tendency for both mean [TP] and [TDP] to be higher from fields that had received some manure in 2017, compared to fields that were not manured. Episodic very high [P] were observed on occasions when high wet-weather tile flow coincided with manure application.
No significant variations in [P] or P export were observed that could be attributed to soil characteristics or to the presence of cover crops on corn
P loads from monitored tile systems in the JBW averaged 0.555 kg/ha/yr and 0.272 kg/ha/yr for TP and TDP, respectively; areal P loads varied by an order of magnitude among the monitored systems.
Monitored P loading in tile drain flow from JBW agricultural fields was in a range comparable to that reported in the literature.

## Slide 44: Conclusions
Tile drainage in the JBW was estimated to contribute ~458 kg TP/yr and ~168-200 kg TDP/yr to the annual 1,913 kg TP/yr and 1,398 kg TDP/yr loads from the watershed to Lake Champlain.
While the apparent contribution of tile drainage of an average of 15% of the annual TP load and 7% of the TDP load is somewhat lower than values reported in the literature, these contributions represent a significant proportion of the annual watershed P load.
In sum, the results of this study confirm the significance of discharge from tile drainage systems in the JBW as a contribution to high P concentrations and loads. Our estimates that tile discharge could contribute up to 24% of watershed TP and up to 15% of TDP loads in Jewett Brook suggest that it will be difficult to accomplish target reductions of agricultural P loads to Lake Champlain without addressing tile drainage.