## Slide 1: Assessment of Tile Drainage System Impacts to Lake Champlain and Phosphorus Loads in Tile Drainage in the Jewett Brook Watershed of St. Albans Bay
Venue: LCBP TAC
Date: May 2, 2018
Presented by: Dave Braun

## Slide 2: This is a study in three parts:
Task 1: Tile Drainage Literature Review (Completed)
  Written by Don Meals and Julie Moore
  252 publications reviewed
  Used as a basis for VTANR’s required tile drain report to legislature, January 2017
Task 2: Monitoring of Tile Drainage Systems (Completed)
  Participation by 6 farmers
  Monitoring 12 tile drains (April 2017 – March 2018)
  Characterization of tile drainage systems
  Continuous flow measurement and composite water sample collection
  Analysis for total and dissolved P and total N
Task 3: P Load Estimation of Tile Drainage Systems (2018)
  Analysis of associations between water quality and agronomic data
  Evaluation of Jewett Brook P load
  Assessment of tile drain P load significance

## Slide 3: Identifiable Tiled Agricultural Fields from Vermont AAFM’s 2015 Cropland Inventory

## Slide 4: Study field and tile drainage system characterization
Site Characterization Report (March 1, 2017) describes:
  Construction of tile drainage systems
  Surface inlets to tile drains
  Crop production in study fields
  Field soil types
  Soil Test P in study fields
  Manure and fertilizer applications
 | Site | Area (A) | Crop | Soil Survey Data % of field, type, slope class, hydrologic group | Soil Test P | Fertilizer Application | Manure Application | Cover Crop
Farmer1 | JBT01 | 25 | 2016: Silage corn 2017: Soybean | 82%: Kingsbury clay, 0 to 3%, D 10%: Massena stony loam, 0 to 3%, C/D 8%: Kingsbury clay, 3 to 8%, D | 7.2 | 2016: starter at plant 2017: starter at plant | 2016: None 2017: None | 2016: None 2017: Unknown
Farmer1 | JBT02 | 4.7 | 2016: Silage corn 2017: Soybean | 69%: Kingsbury clay, 3 to 8%, D 31%: Kingsbury clay, 0 to 3%, D | 9.3 | 2016: starter at plant 2017: starter at plant | 2016: None 2017: None | 2016: None 2017: Unknown
Farmer1 | JBT04 | 5.7 | 2016: Silage corn 2017: Soybean | 100%: Kingsbury clay, 0 to 3%, D | 4.5 | 2016: starter at plant 2017: starter at plant | 2016: None 2017: None | 2016: None 2017: Unknown

## Slide 5: Tile drainage system construction
  All 12 systems selected are standard, perforated, corrugated drain pipe.
  Most were installed within the last decade.
  The outfalls range in diameter from 4–12 inches.
  9 of the 12 tile drains discharge to ditches. The 3 remaining (JBT01, JBT02, and JBT04) discharge directly to Jewett Brook.
  The tile drains range from 3–5 feet below ground, with most in the 3–4 feet range.
  All study fields have patterned drainage except JBT16, which has a dendritic (branching) system.
  Drain spacing is in the typical range of 25–40 feet, with the exception of JBT18 and JBT19, which have 80-foot spacing.

## Slide 6: Surface inlet to JBT14 tile drain (3 systems have known inlets; blind inlets also possible)

## Slide 7: Monitoring manhole construction

## Slide 8: JBT11 monitoring station

## Slide 9: Typical instrument shelter (JBT11)

## Slide 10: Waterflux 3000 flowmeter at JBT11, April 20, 2017

## Slide 11: JBT01 flow rate
TP: 14.7 µg/L
TDP: 9.7 µg/L
TN: 2.45 mg/L
Chart: Flow rate (L/min)

## Slide 12: JBT11 flowing clear, April 20, 2017
TP: 14.7 µg/L
TDP: 9.7 µg/L
TN: 2.45 mg/L

## Slide 13: Tile drain muddying already turbid Jewett Brook

## Slide 14: JBT01 flowing muddy, November 3, 2017
TP: 329 µg/L
TDP: 60.1 µg/L

## Slide 15: JBT06 field on October 27, 2017 after manure injection
TP: 1,884 µg/L
TDP: 1,576 µg/L

## Slide 16: Distributions of Total P EMCs (April – Nov. 2017)
JBT13: TP=35,295 µg/L (excluded)
Samples following manure application

## Slide 17: Distributions of TDP EMCs (April – Nov. 2017)

## Slide 18: Distributions of Total P EMCs (April – Nov. 2017) Samples following manure application removed

## Slide 19: Distributions of Total N EMCs (April – Nov. 2017)
JBT13: TN=217 mg/L (excluded)

## Slide 20: Questions:
In progress:
Associations between WQ and AG variables
Proportion of Jewett Brook P load contributed by tile drains
Three related research questions / farmer concerns
Are surface inlets the main route for P transport to tile drains, particularly where we find high P concentrations following manure application?
Are conditions in the Jewett Brook watershed representative of conditions in the wider Lake Champlain Basin?
Given multiple tradeoffs between surface runoff and subsurface drainage, is the net effect of tile drainage increased or decreased P export?

## Slide 21: Thank you
Dave Braun
dbraun@stone-env.com
(802) 272-8819

## Slide 22: Runoff and Erosion on Tiled Field (JBT14)

## Slide 23: 90-degree V Weir and Level Sensor at JBT06

## Slide 24: Station JBT01