## Slide 1: Agricultural Practice Monitoring and Evaluation in the Vermont Portion of the Lake Champlain Basin: Evaluation of the Effects of Grassed Waterways
Date: May 3, 2017
Presented by: Dave Braun
Conference/Venue: Lake Champlain Basin Program TAC Meeting

## Slide 2: Participating Organizations
USDA-NRCS
Vermont Agency of Agriculture, Food, and Markets
Vermont Department of Environmental Conservation
Lake Champlain Basin Program
Cooperating farmers

## Slide 3: Farm Locations
16 paired runoff monitoring stations on seven farms in the Vermont portion of the Lake Champlain Basin

## Slide 4: Practices Evaluated
1. Soil aeration on hay prior to manure application
  Ferrisburgh, Shelburne, Shoreham
2. Reduced tillage with manure injection on corn
  Franklin, Williston
4. Water and sediment control basin (WASCoB)
  Franklin
3. Cover cropping on corn
  Pawlet
5. Grassed waterway
  Charlotte
Notes: Complete GIS Build-out Analysis: 1.98” horizontal, 0.9” vertical, text anchored at bottom
Bulleted box: 1.9” horizontal, 1.93” vertical, text anchored at top
Image: 0.5” horizontal, 0.5” vertical
Logo: 8” horizontal, 7.91” vertical

## Slide 5: Aeration Slots

## Slide 6: Typical cover crop on PAW1 field, April 19, 2016

## Slide 7: What does the work plan say? (revised Dec. 2015)
PART 1
Monitoring of Ferrisburgh, Franklin, and Pawlet sites extended through 2015
Monitoring of the Shoreham site extended through 2016
  Monitoring equipment replacement and repair
  Monitoring operations
  Data management, analysis, and reporting
  Practice evaluation and site decommissioning (FER, FRA, PAW, SHO, WASCoB)

## Slide 8: Results
Number of paired events with valid data at both stations, 2012 – Dec. 31, 2016
 | Calibration Period |  | Treatment Period | 
Station | Number of Paired Flow Events1 | Number of Paired Chemistry Events | Number of Paired Flow Events1 | Number of Paired Chemistry Events
CHA | 9(9) | 9(9) | NA | NA
FER | 23 | 21 | 18(3) 2 | 15(3) 2
FRA | 14 | 9 | 16 | 13(1) 2
PAW | 40 | 29 | 20(2) 2 | 16(4) 2
SHE | 27 | 20 | 25(5) 2 | 24(5) 2
SHO | 13 | 10 | 10 | 8
WIL | 18 | 15 | 4(1) 2 | 3(1) 2
1 Includes only events with measureable runoff and valid data at both stations in a pair 2 Event number in parentheses are not included in statistics in the Year 4 report |  |  |  | 

## Slide 9
Comparisons across study watersheds

## Slide 10: All stations
[TP]: WIL/CHA > FER/FRA/SHO > SHE/PAW Grand mean = 486 µg/L

## Slide 11: All stations
[TN]: CHA/FRA > WIL/FER/SHO > SHE/PAW
Grand mean = 2.85 mg/L

## Slide 12: All stations
[TSS]: FRA/PAW/WIL > CHA/FER > SHE/SHO
Grand mean = 33.3 mg/L

## Slide 13: All stations
[%DP]: SHE/SHO/FER/CHA > FRA/PAW/WIL

## Slide 14: All stations
[%DN]: SHO/FER/CHA > SHE/FRA> PAW/WIL

## Slide 15: Relationships between Soil P and Median P EMCs in Runoff from Study Watersheds

## Slide 16: Franklin
  Calibration data from 9-14 events; Treatment data from 14-16 events
  Excellent calibration and treatment period regression relationships between FRA 1 (treatment) and FRA2 (control)
Variable | Significance | Response to treatment
HQ | n.s | No change in HQ
TP | n.s | (Increase in [TP])
TDP | 0.021 | Increase in [TDP]
TN | n.s | (Decrease in [TN])
TDN | n.s | (Decrease in [TDN])
TSS | n.s | (Increase in [TSS])
Cl | n.s | (Increase in [Cl])
TPx | n.s | No change in TPx
TDPx | n.s | No change in TDPx
TNx | n.s | No change in TNx
TDNx | n.s | No change in TDNx
TSSx | n.s | (Increase in TSSx)
Clx | n.s | No change in Clx

## Slide 17: Franklin
FRA | Ctl mean | CAL model | TRT model | ∆ | % change
[TDP] (ug/L) | 226 | 240 | 268 | +28 | +12%

## Slide 18: Summary
Site | Crop | Treatment | Response
FRA | Corn | Injection | [TDP]
WIL | Corn | Injection | 
SHE | Hay | Aeration | Q [TN], [TDN], [TSS] [Cl], TPx, TDPx, TDNx, Clx
FER | Hay | Aeration | [TP], [TN], [TDN]
SHO | Hay | Aeration | [TDP], TPx, TDPx, TNx, TDNx, TSSx, Clx
PAW | Corn | CC | [TSS], TPx, TSSx

## Slide 19: Why didn’t we see a better response to treatment?
  Practices were poorly implemented or misapplied in some cases
      Once the wrong field was aerated (at SHO)
      Once the wrong field was cover cropped (PAW)
      Once both watersheds were chisel plowed rather than the intended one (WIL)
      Generally poor cover crop establishment (PAW)
      Less-than-equal manure applications (especially FER)
  Learning curve - it often takes a few years for farmers to get up to speed with a new practice or piece of equipment
  Certain practices (e.g., conservation tillage and cover crops) are not expected to yield their full benefits until they have been consistently applied over longer time spans
  Statistical analyses included data gathered year-round (including some winter events) whereas certain practices should be most effective shortly after installation
  Confounding environmental conditions
    Extended dry periods during 2014 and 2015 growing seasons
    Weed growth on cover crop control field
  Heaved flumes and attendant ponding (significant at SHE)
  Are these the appropriate practices to control dissolved P and N?

## Slide 20: Consider need for data stratification and exploratory analysis
Incorporate additional monitoring data at selected sites (PAW, FER, SHE)
Stratifying data by time– value of considering immediate and longer-term effects of treatment practices
  In current analysis, all events are given equal weight
  Many treatment are far removed from the next rainfall event
Stratifying data by flow
  In current analysis, all events are given equal weight, regardless of their magnitude.
  In certain paired watershed pairs (notably SHE), different hydrologic relationships may exist across a range of event magnitudes. Moderate and large events during which significant field areas contribute runoff may reveal treatment effects not observed during smaller events.

## Slide 21: What does the work plan say? (revised Dec. 2015)
PART 2
Evaluation of the Effects of Grassed Waterways (CHA)
  QAPP preparation
  Site characterization and monitoring facility design and construction
  Monitoring operations through 2018
  Data management, analysis, and reporting
  Practice evaluation and site decommissioning

## Slide 22: Charlotte Study Watersheds
CHA1 = Control
CHA2 = Treatment

## Slide 23: CHA1 station

## Slide 24: CHA2 Flume in Winter

## Slide 25: CHA2 Flume and Gully

## Slide 26: Instrument Shelter
18 paired runoff events successfully monitored through December 2016.
An additional 6 events monitored between January and April 2017.
Very few events recorded in 2016 Q2 and Q4 and none in Q3.

## Slide 27: Charlotte
Calibration data from 9 paired events, 10/1/2015 – 2/5/2016
  >90% of P and N in dissolved form
  Excellent regressions between CHA1 (Control) and CHA 2 (Treatment)
r2 = 0.98

## Slide 28: Gully Formed in CHA2 Watershed

## Slide 29: Assessment of Tile Drainage System Impacts to Lake Champlain and Phosphorus Loads in Tile Drainage in the Jewett Brook Watershed of St. Albans Bay
Date: May 3, 2017
Presented by: Dave Braun
Conference/Venue: Lake Champlain Basin Program TAC Meeting

## Slide 30: What does the work plan say?
Task 1: Literature Review Examining Tile Drainage Systems
  Secondary data QAPP preparation
  Literature review
  Synthesis and reporting
Task 2: Monitoring and Assessment of Tile Drainage Systems
  Primary data QAPP preparation
  Characterization of tile drainage systems (Characterization report)
  Study implementation (Installation report/Monitoring summaries)
  Data management and analysis (Monitoring and Assessment report)
Task 3: P Load Estimation of Tile Drainage Systems in the Jewett Brook Watershed
  Evaluation of tributary P load (Technical memo)
  Assessment of tile drain P load significance (Final Report)

## Slide 31: Literature Review
Written by Don Meals and Julie Moore
252 references were obtained and reviewed
Reviewed by TAC and revised accordingly
Used as a basis for VTANR’s required tile drain report to the Vermont legislature, January 2017
“This literature review synthesizes the current state of knowledge concerning the effects of subsurface drainage on hydrology, reported P concentrations and loads in subsurface drainage water, and major factors influencing the loss of P through subsurface drainage, derived from published scientific research. The review also briefly identifies techniques of drainage management and treatment to reduce P losses.”

## Slide 32: Study Field and Tile Drainage System Characterization
Characterization Report (March 1, 2017) describes:
  Construction of tile drainage systems
  Surface inlets to tile drains
  Crop production in study fields
  Field soil types
  Soil Test P in study fields
  Manure and fertilizer applications
 | Site | Area (A) | Crop | Soil Survey Data % of field, type, slope class, hydrologic group | Soil Test P | Fertilizer Application | Manure Application | Cover Crop
Farmer1 | JBT01 | 25 | 2016: Silage corn 2017: Soybean | 82%: Kingsbury clay, 0 to 3%, D 10%: Massena stony loam, 0 to 3%, C/D 8%: Kingsbury clay, 3 to 8%, D | 7.2 | 2016: starter at plant 2017: starter at plant | 2016: None 2017: None | 2016: None 2017: Unknown
Farmer1 | JBT02 | 4.7 | 2016: Silage corn 2017: Soybean | 69%: Kingsbury clay, 3 to 8%, D 31%: Kingsbury clay, 0 to 3%, D | 9.3 | 2016: starter at plant 2017: starter at plant | 2016: None 2017: None | 2016: None 2017: Unknown
Farmer1 | JBT04 | 5.7 | 2016: Silage corn 2017: Soybean | 100%: Kingsbury clay, 0 to 3%, D | 4.5 | 2016: starter at plant 2017: starter at plant | 2016: None 2017: None | 2016: None 2017: Unknown

## Slide 33: Tile Drainage System Construction
All 12 systems selected are standard, perforated, corrugated drain pipe.
Most were installed within the last decade.
The outfalls range in diameter from 4–12 inches.
9 of the 12 tile drains discharge to ditches. The 3 remaining (JBT01, JBT02, and JBT04) discharge directly to Jewett Brook.
The tile drains range from 3–5 feet below ground, with most in the 3–4 feet range.
All study fields have patterned drainage except JBT16, which has a dendritic (branching) system.
Drain spacing is in the typical range of 25–40 feet, with the exception of JBT18 and JBT19, which have 80-foot spacing.

## Slide 34: Identifiable Tiled Agricultural Fields from AAFM’s 2015 Cropland Inventory

## Slide 35: Monitoring Manhole Construction

## Slide 36: Monitoring Manhole Construction

## Slide 37: Monitoring Manhole Construction

## Slide 38: Waterflux 3000 Flowmeter at Station JBT11

## Slide 39: JBT11 Monitoring Station

## Slide 40: Typical Instrument Shelter (JBT11)

## Slide 41: Station JBT01

## Slide 42: Weir Box Constructed at Station JBT06

## Slide 43: 90-degree V Weir and Level Sensor at JBT06

## Slide 44: Flow Proportional Sampling at JBT06

## Slide 45: Comparing Flow at JBT06 with CHA1 and CHA2

## Slide 46: Monitoring Start Dates
Station | Start flow monitoring | Start autosampling | Current condition
JBT01 | 3/23/17 | 4/5/17 | OK
JBT02 | 3/23/17 | 4/5/17 | OK
JBT04 | 4/3/17 | 4/5/17 | OK
JBT05 | 4/20/17 | 4/20/17 | 1) Waterflux flowmeter bad; ISCO 2150 AV flowmeter temporarily substituted 2) Replacement modem requires activation
JBT06 | 4/5/17 | 4/5/17 | OK
JBT07 | 3/30/17 | 4/5/17 | OK
JBT11 | 4/5/17 | 4/5/17 | Modem problem (power)
JBT13 | 4/3/17 | 4/11/17 | OK
JBT14 | 4/5/17 | 4/5/17 | Modem problem (clock)
JBT16 | 3/30/17 | 4/5/17 | OK
JBT18 | 4/22/17 | 4/22/17 | OK
JBT19 | 4/22/17 | 4/22/17 | OK

## Slide 47: TP, TDP, and TN in Weekly Composite Samples April 11, 2017 Collection Date (first round)
Station | TP (ug/L) | TDP (ug/L) | TN (mg/L)
JBT01 | 491 | 258 | 4.8
JBT02 | 976 | 678 | 7.2
JBT04 | 798 | 120 | 4.9
JBT05 | NS | NS | NS
JBT06 | 195 | 131 | 33
JBT07 | 708 | 159 | 7.5
JBT11 | 40 | 58 | 3.3
JBT13 | NS | NS | NS
JBT14 | 248 | 66 | 7.4
JBT16 | 105 | 73 | 5.8
JBT18 | NS | NS | NS
JBT19 | NS | NS | NS

## Slide 48: Standpipe Inlet to JBT14 Tile Drain

## Slide 49: Tile Drain Muddying Already Muddy Jewett Brook

## Slide 50: Runoff and Erosion on Tiled Field (JBT14)

## Slide 51: Feasibility Evaluation of Phosphorus Removal via Engineered Ecosystems in the St. Albans Bay Watershed
Date: May 3, 2017
Presented by: Dave Braun
Conference/Venue: Lake Champlain Basin Program TAC Meeting

## Slide 52: Why Jewett Brook?

## Slide 53: What does the work plan say?
Objective: to evaluate the feasibility, from a regulatory standpoint, of developing an “engineered ecosystem” treatment train to remove phosphorus from Jewett Brook before it flows into St. Albans Bay.
Task 1: Establish Evaluation Criteria and Project Advisory Group (Summary report)
Task 2: Secondary Data QAPP preparation
Task 3: Analysis of Regulatory Acceptability (Summary report)

## Slide 54: Schedule
Task | Deliverable | End Date
Quarterly Progress Reports | Quarterly progress reports | July 10, 2017 October 10, 2017 January 10, 2018
Task 1: Establish Evaluation Criteria | Summary report of committee deliberations and defined criteria | November 30, 2017
Task 2: Quality Assurance Project Plan (QAPP) | Approved Secondary Data QAPP | 6-8 weeks following contract execution
Task 3: Analysis of Regulatory Acceptability | Progress summarized in quarterly reports Findings described in Summary report | October 10, 2017
Final Summary Report | Summary report and presentation to TAC | March 30, 2018

## Slide 55: Title with large image only

## Slide 56: Title with large image only

## Slide 57: Thank you.
For more information: dbraun@stone-env.com