## Slide 1: Assessment of Tile Drainage System Impacts to Lake Champlain and Phosphorus Loads in Tile Drainage in the Jewett Brook Watershed of St. Albans Bay
Date: December 21, 2017
Presented by: Dave Braun
Conference/Venue: Tile Drain Advisory Group Meeting

## Slide 2: This is a study in three parts:
Task 1: Tile Drainage Literature Review (Completed)
  Written by Don Meals and Julie Moore
  252 publications were reviewed
  Used as a basis for VTANR’s required tile drain report to the Vermont legislature, January 2017
Task 2: Monitoring of Tile Drainage Systems (In Progress)
  Participation by 6 farmers
  Monitoring of 12 tile drains (April 2018 – April 2019)
  Characterization of tile drainage systems
  Continuous flow measurement and composite sample collection
  Analysis for total and dissolved P and total N
Task 3: P Load Estimation of Tile Drainage Systems (2019)
  Analysis of associations between water quality and agronomic data
  Evaluation of Jewett Brook P load
  Assessment of tile drain P load significance

## Slide 3: Study Field and Tile Drainage System Characterization
Characterization Report (March 1, 2017) describes:
  Construction of tile drainage systems
  Surface inlets to tile drains
  Crop production in study fields
  Field soil types
  Soil Test P in study fields
  Manure and fertilizer applications
 | Site | Area (A) | Crop | Soil Survey Data % of field, type, slope class, hydrologic group | Soil Test P | Fertilizer Application | Manure Application | Cover Crop
Farmer1 | JBT01 | 25 | 2016: Silage corn 2017: Soybean | 82%: Kingsbury clay, 0 to 3%, D 10%: Massena stony loam, 0 to 3%, C/D 8%: Kingsbury clay, 3 to 8%, D | 7.2 | 2016: starter at plant 2017: starter at plant | 2016: None 2017: None | 2016: None 2017: Unknown
Farmer1 | JBT02 | 4.7 | 2016: Silage corn 2017: Soybean | 69%: Kingsbury clay, 3 to 8%, D 31%: Kingsbury clay, 0 to 3%, D | 9.3 | 2016: starter at plant 2017: starter at plant | 2016: None 2017: None | 2016: None 2017: Unknown
Farmer1 | JBT04 | 5.7 | 2016: Silage corn 2017: Soybean | 100%: Kingsbury clay, 0 to 3%, D | 4.5 | 2016: starter at plant 2017: starter at plant | 2016: None 2017: None | 2016: None 2017: Unknown

## Slide 4: Tile Drainage System Construction
  All 12 systems selected are standard, perforated, corrugated drain pipe.
  Most were installed within the last decade.
  The outfalls range in diameter from 4–12 inches.
  9 of the 12 tile drains discharge to ditches. The 3 remaining (JBT01, JBT02, and JBT04) discharge directly to Jewett Brook.
  The tile drains range from 3–5 feet below ground, with most in the 3–4 feet range.
  All study fields have patterned drainage except JBT16, which has a dendritic (branching) system.
  Drain spacing is in the typical range of 25–40 feet, with the exception of JBT18 and JBT19, which have 80-foot spacing.

## Slide 5: Standpipe Inlet to JBT14 Tile Drain

## Slide 6: Monitoring Manhole Construction

## Slide 7: Monitoring Manhole Construction

## Slide 8: JBT11 Monitoring Station

## Slide 9: Typical Instrument Shelter (JBT11)

## Slide 10: Waterflux 3000 Flowmeter at JBT11, April 20, 2017
TP = 16.2 µg/L
TDP = 11.5 µg/L
TN = 2.59 mg/L

## Slide 11: Flow Proportional Sampling at JBT06

## Slide 12: Tile drain muddying already turbid Jewett Brook

## Slide 13: JBT01 flowing muddy, November 3, 2017
TP = 360 µg/L
TDP = 46.5 µg/L

## Slide 14: JBT06 field on October 27, 2017 after manure injection
TP = 1,884 µg/L
TDP = 1,576 µg/L

## Slide 15: Distributions of Total P EMCs (April – Nov., 2017)
JBT13: TP=35,295 µg/L (excluded)

## Slide 16: Distributions of Total Dissolved P EMCs (April – Nov., 2017)

## Slide 17: Distributions of Total N EMCs (April – Nov., 2017)
JBT13: TN=217 mg/L (excluded)

## Slide 18: Thank you.
Dave Braun
dbraun@stone-env.com
(802)272-8819

## Slide 19: Identifiable Tiled Agricultural Fields from AAFM’s 2015 Cropland Inventory

## Slide 20: Runoff and Erosion on Tiled Field (JBT14)

## Slide 21: Monitoring Manhole Construction

## Slide 22: Weir Box Constructed at Station JBT06

## Slide 23: 90-degree V Weir and Level Sensor at JBT06

## Slide 24: Station JBT01

## Slide 25: Comparing Flow at JBT06 with CHA1 and CHA2

## Slide 26: Monitoring Start Dates
Station | Start flow monitoring | Start autosampling | Current condition
JBT01 | 3/23/17 | 4/5/17 | OK
JBT02 | 3/23/17 | 4/5/17 | OK
JBT04 | 4/3/17 | 4/5/17 | OK
JBT05 | 4/20/17 | 4/20/17 | 1) Waterflux flowmeter bad; ISCO 2150 AV flowmeter temporarily substituted 2) Replacement modem requires activation
JBT06 | 4/5/17 | 4/5/17 | OK
JBT07 | 3/30/17 | 4/5/17 | OK
JBT11 | 4/5/17 | 4/5/17 | Modem problem (power)
JBT13 | 4/3/17 | 4/11/17 | OK
JBT14 | 4/5/17 | 4/5/17 | Modem problem (clock)
JBT16 | 3/30/17 | 4/5/17 | OK
JBT18 | 4/22/17 | 4/22/17 | OK
JBT19 | 4/22/17 | 4/22/17 | OK

## Slide 27: TP, TDP, and TN in Weekly Composite Samples April 11, 2017 Collection Date (first round)
Station | TP (ug/L) | TDP (ug/L) | TN (mg/L)
JBT01 | 491 | 258 | 4.8
JBT02 | 976 | 678 | 7.2
JBT04 | 798 | 120 | 4.9
JBT05 | NS | NS | NS
JBT06 | 195 | 131 | 33
JBT07 | 708 | 159 | 7.5
JBT11 | 40 | 58 | 3.3
JBT13 | NS | NS | NS
JBT14 | 248 | 66 | 7.4
JBT16 | 105 | 73 | 5.8
JBT18 | NS | NS | NS
JBT19 | NS | NS | NS